## Slide 1: EP1000
3D Models

## Slide 2: Essential Tools in Fusion 360
From Autodesk Training
  Introduction to Fusion 360
  User Interface Overview
  Open, close, export, upload, and save designs
  Set Preferences
  Adjust Display settings
  Use the Marking Menu
  Use the Toolbox
  Create A Project
  Open a Design created in another CAD system
  Components and Bodies
  Parametric vs. direct modeling
  Working with Design versions
  Sketch Constraints

## Slide 3: Fast Track for Engineers
Kevin Kennedy Product Design Online
  Recommended: Learn Fusion 360 in 30 days
  Highlighted Topics
    Navigating the Fusion 360 User Interface (sections explained) - REVISED 2019
    Default settings for Fusion 360
    How to Manually Add Sketch Constraints - Learn Autodesk Fusion 360 in 30 Days: Day #16
    How to Create text in Fusion 360
    How and Why to Fully Constrain Your Sketches

## Slide 4: Fusion 360 Building Blocks
Sketch
  Created in a 2D plane
  Sketches should be constrained and closed
  Forms the building block of all models
Body
  Usually created from a sketch(s)
  Is a SOLID
  Can combine to form other bodies
Component
  Made up of bodies and sketches
  Usually "joined" or "combined“
  Can be used to form other components

## Slide 5: Constraints
Why constrain a sketch?
  A constrained sketch cannot be changed (accidentally).
  Each segment is locked by a dimension or a constraint.
  Constrained segments are drawn in BLACK
    Kevin Kennedy: How and Why to Fully Constrain Your Sketches

## Slide 6: Types Of Constraints
  Dimension
  Horizontal, Vertical
  Coincident (constrains a point to another point, line, arc, or curve.)
  Tangent
  Equal
  Parallel
  Perpendicular
  Fix / UnFix
  MidPoint
  Concentric
  Colinear ( constrains a line to another line, so that both lines fall onto the same line)
  Symmetry
  Curvature

## Slide 7: Saving Designs
Fusion 360 saves all files into the cloud
  You can share your files within the cloud
  You can export your design file to the local storage using export.
  Output format is .f3d

## Slide 8: Parametric Design
Enter variables as parameters
Use parameters in your design
Design becomes very flexible

## Slide 9: E.g. Parametric Polygon
A fully configurable polygon with parametric sides and size.
Try changing the parameters

## Slide 10: Methods of Creating 3D Models
Extrusion
  Use a 2D plane profile
  Extend into the 3rd plane
Rotation
  Use a 2D plane profile
  Rotate the plane around an axis
Sculpting
  Start with a 3D object
  Add, remove 3D objects
  Subdivide the surface into sections
  Push, pull, extend, contract sections

## Slide 11: Extrusion
Start with a 2D closed profile in plane
Stop Sketch
Create > Extrude in 3rd axis

## Slide 12: Extrude – Join / New Body
You can build new bodies by adding/creating the original.

## Slide 13: Extrude – Cut
You can cut holes using subtraction to the original..

## Slide 14: Extrude - options
Start
Direction
Extent Type
Operation

## Slide 15: Exercise 1: Name Tag
Let's make a name tag
  dimensions: 30mm x 70mm x 4 mm
  rim of 1.5mm thickness around the edges, height 2.5mm
  key-ring hole of 4mm, re-enforced with 1.5mm rim
  name or design/pattern 0.5mm below surface
  base of name tag 1.5mm thick

## Slide 16: Modify > Shell
Makes a shell of the solid object
Starts with the face that was selected
The shell thickness must be specified

## Slide 17: Create > Loft
Create a solid object from profiles on different planes

## Slide 18: Exercise 2: A Lego brick
This is Kevin Kennedy’s video tutorial on the drawing of a Lego brick. https://youtu.be/6yPKMSb6ja8

## Slide 19: Exercise 3: Extrudes & Planes
This object is made up of 20 cubes (20mm) glued together and then shelled to a thickness of 4mm

## Slide 20: EP1000
3D Models
End