## Slide 1: EP1000
A Short Introduction to Electricity & Electronics

## Slide 2: What is electricity?
Youtube: The Engineering Mindset Electrical Engineering Basics Playlist

## Slide 3: Electronic Components
YouTube: Great Scott! Essential Electronics Components that you will
need for creating projects!
Open University: An Introduction to Electronics

## Slide 4: Electricity
The flow of electrons in a closed circuit.
Voltage is the difference in electrical potential between 2 points (volts)
Current is the rate of flow of electrical charge past a point (amps)
Resistance is a measure of the opposition to the flow of electronics (ohms)

## Slide 5: Types of electrical currents
Alternating current (AC) where voltage moves from positive to negative values
E.g. Home electricity
Direct current (DC) where the potential is at a fixed value
E.g. Battery

## Slide 6: Ohm’s Law
Voltage = Current * Resistance
Resistance calculation
  Series
  Parallel
+

## Slide 7: Kirchoff’s Laws
Current Law At any junction, or node, in an electrical circuit, the sum of the currents flowing into the node is the sum of the currents flowing out of a node.
Voltage Law When the direction is taken into account, the sum of the potential differences in any closed circuit is zero.

## Slide 8: Electrical components
Insulators Do NOT allow current to flow
Conductors Do allow current to flow
Semiconductors Allows current to flow if some electrical conditions are met e.g. diodes.

## Slide 9: Common components
Wires - Dupont connector wires
Switches
Resistors - Variable resistors, potentiometers
Capacitors
Inductors (seldom used)
Diodes - LED (Light Emitting Diodes)
Semiconductors - 555 Timer, Voltage Regulators
Microcontrollers – Arduino family
YouTube: bigclivedotcom – A Simple Guide to Electronic components

## Slide 10: TinkerCAD
Allows creation of simple 3D designs
Circuits – allows simulation of
  Electronic circuits
  Arduino interfacing with Processing/C++
  Micro-bit interfacing with CodeBlocks

## Slide 11: Ohms Law
Change the value of R, check V=IR
Voltage is measured with voltmeter in parallel Current is measured with amp-meter in series
Volt-meter
Amp-meter

## Slide 12: Working with a Breadboard
Breadboard used in many prototyping projects.
Quick testing of circuits
Circuit checks effect of R with LED

## Slide 13: Electronic Symbols
Provides a short-cut method of drawing/expressing electronics circuits

## Slide 14: LED Circuit
We use schematics to represent the electrical circuits we create.
We need to be able to transform from a schematic to a layout and vice versa.

## Slide 15: Assignment
Convert the schematic into TinkerCAD circuits and simulate it.
This assignment is not graded.

## Slide 16: Expected Result
The 555 timer is configured as an astable using R and C values.
The result is an alternating ON/OFF signal which flashes the LED

## Slide 17: Hints & Tips
Assignment sheet: Electronics
Good references:
  Introduction to TinkerCAD Circuits
  Introduction to TinkerCAD Digital
  Introduction to Function Generator & Oscilloscope
You will be asked to implement the circuit on an actual breadboard in the lab.
Document your experiences

## Slide 18: EP1000
A Short Introduction to Electricity & Electronics
End