## Slide 1: EP1000
Computer Controlled Cutting

## Slide 2: Computer Controlled Cutting
Perform Cutting operations based on digital data.
Also known as CNC (Computer Numerical Control)
Data is provided from:
  CADD operations
  Digital 2D drawings
Provides accurate and precise cutting operations
Used in:
  Laser cutting & engraving
  Flatbed cutters & 2D routers
  Milling machines

## Slide 3: 2D profile
All cutting systems work on a 2D profile which provides an outline of the cut.
Advantages:
  The cut is precise with little wastage of material.
  Allows positioning to prevent wastage.
  Repeatability
Vector File formats:
  DXF (Data eXchange Format)
  PDF (Portable Document Format)
  SVG (Scalable Vector Graphics)

## Slide 4: Vector Software
2D Vector drawing programs: Inkscape, AutoCAD
CADD Software – Fusion 360
Don’t forget InkScape !

## Slide 5: Software Tools
Fusion 360
  Full CAD/CAM software to obtain profiles
  Lots of modelling tools to help
Vector Drawing software
  Inkscape
  LibreCAD (for DXF files)
  CorelDraw (licensed software)
Output Vector formats
  DXF (outdated, but still used, text editable)
  PDF, EPS
  SVG (may have different variants)
  AI (Adobe Illustrator format)

## Slide 6: Exercise 1: Keychain for cutting
Let's make a keychain for the fablab with logo
Size: 30mm x 70mm x Thickness (dependent on material)

## Slide 7: What happens when cut
Islands may form, these drop out after cutting
Need to edit the Vector file before cutting
Placement of causeways to prevent drop-outs
Post production (i.e. edit DXF exported file)

## Slide 8: Post Production Editing
Use a Vector Drawing program to create the causeways
May need knowledge of vector drawing program
Suggest CorelDraw

## Slide 9: Fusion 360 Explode Text
Use the Explode Text function to separate each letter in the word.
Add causeways in Fusion 360 before extrusion for cut surface

## Slide 10: Fusion 360: Export Cut Profile -1
Create your design
Extrude surfaces to create object

## Slide 11: Fusion 360: Export Cut Profile -2
New sketch on object profile to cut
Click again on profile to verify/select

## Slide 12: Fusion 360: Export Cut Profile -3
New sketch created
Should rename to avoid confusion (design_dxf)
R-Click on sketch name
Save As DXF

## Slide 13: DXF format
A simple text format that defines the coordinates of the profile.
Can come in different versions
Backward compatible only

## Slide 14: Fusion 360: Modelling
Modelling allows us to simulate the actual object using CADD
We can use CADD tools to help us in the design
Most common tools are:
  Combine
  Joints
  Cross-sectional views
  Clearances

## Slide 15: Let’s make a joint
We will use the CADD features to assist us
We would like to join 2 pieces of wood

## Slide 16: Drawing Parameters

## Slide 17: Draw the 2 components
We would like a “tight” fit, since we are going to CCC the wood.
The cuts will be very precise.
(The joint is exaggerated to show the effect)

## Slide 18: Use CADD to effect the joint
Modify > Combine
Creates the joint and necessary cuts without further drawing
Blue = Target Body
Red = Tool Body
Operation = Cut
Keep tools

## Slide 19: Laptop Stand
Let’s quickly design a laptop stand that can be lasercut.
4 components
legs (x2)
top
front support
rear support

## Slide 20: Legs
Set your own parameters

## Slide 21: Create the body and a copy of the leg
Extrude the profile using thickness
Move/Copy the body
Length of laptop

## Slide 22: Add Component - Top
Create component Top
Enable the component!
Create new sketch, select slope surface
Top should line up with the top edge of the legs
Bottom should line up with the slip support stop
Sides extend 20mm on each side
Extrude the top

## Slide 23: ..so far .. so good!
You should have 2 components.
Use Inspect > Component Color Cycling

## Slide 24: Fusion 360 History/Playback bar
We can use the History/Playback bar to walk through and edit (sometimes) changes
Let’s add supports for our top so that it does not move while we use it

## Slide 25: Edit/Add flanges to the legs
Use the history bar to add the flange
The rest of the design will auto-correct itself to accommodate the change

## Slide 26: Modify > Combine
Use the combine function to cut the slots into the top
Remember to “keep tools” after cutting

## Slide 27: Add front support
The front support adds strength to the frame
Offset the spar from the front e.g. 40mm
Protrude the side for support
Use Combine to cut the slots on the legs

## Slide 28: Add back support
Create new component
Create offset plane from back leg
Create new sketch
Draw structure, ensure constraints
Modify > Combine to cut out the slots

## Slide 29: Completed Model
Move the bodies and examine the result
Check for clearances and cuts

## Slide 30: Finishing touches
Fillet (smooth) the edges
Fillet/Chamfer the joints for easy insertion

## Slide 31: Export & check the DXF for cutting
For each body
  Turn off other components/bodies
  Create new sketch for cut profile
  Rename the sketch for reference
  Export to DXF
Use LibreCAD to check or layout the cuts

## Slide 32: Task: Draw your laptop stand
Draw your own laptop stand (measure your laptop)
Add features (?)
Ref: https://youtu.be/7riGolu7BpA

## Slide 33: EP1000
Computer Controlled Cutting
End